## Slide 1: Block Stacking Robot
Abigail Egya-Mensah, Frank Laubach

## Slide 2: INTRODUCTION
This project’s objective is to enable the robot to accurately perceive block positions and orientations and stack them in the desired configuration.
The program will be tested and evaluated using the Emika Franka arm in the PyBullet simulator, which provides a safe and controlled environment to simulate the robot and the blocks. We implemented the Inverse-kinematics code from HW 6.
The Implemented Methods aside the baseline are
Harris Corner Detection
Haar Cascades

## Slide 3: PSEUDOCODE
Prepare simulator
Spawn three (7cm x 7cm) cubes in random locations
Spawn camera and take a picture
Give the image to a method
Method gives coordinates and orientation
Run through the block-stacking loop 3 times

## Slide 4: HAAR CASCADE
This function was implemented in Python using the OpenCV library. It works by applying a set of pre-defined Haar features to the image and using them to classify whether a region of the image contains the object of interest or not. It is designed for object detection based on image features, and does not have a built-in capability for detecting the orientation of objects.
A Classifier is need for Haar Cascade Implementation. The following steps were used to generate a classifier:
Generate negative and positive samples
Train classifier using the opencv_traincascade command
Test the trained classifier on a new image using the detectMultiScale method of the CascadeClassifier class from Opencv

## Slide 5: HAAR CASCADE - CONT.
Implement the classifier in the Haar function code. Once the blocks have been detected using the Haar Cascade classifier, the code calculates the x and y position of the center of each block and converts it to meters based on the provided workspace. The calculated x and y positions are stored in the x_meters and y_meters lists, respectively.

## Slide 6: HARRIS POINTS
The method convolves the image using directional weights to get Ix and Iy
Ix and Iy → IxIx, IyIy, and Ixy
→ structure tensor M, Harris values R
Harris values are filtered to give Harris points

## Slide 7: HARRIS POINTS - CONT.
Squares are fit to the Harris points
‘Scores’ are calculated based on nearby points
The highest scoring square is found
  neighboring test squares eliminated
Repeat 3x for 3 locations
Scores Low
Scores High

## Slide 8: EXPERIMENTS
20 trials were run for each method
3 random blocks
Each method scored on detection, grasp success, and time

## Slide 9: ANALYSIS
Baseline method (giving the robot arm the location) was perfect
Harris method
  97% detection
  83% grasp
    Due to inverse-kinematics issue
  98 second execution time
Haar method
  100% detection
  55% grasp
    Cannot detect orientation
    1 second execution time

## Slide 10: CONCLUSION
Haar Method
  Perfect detection
  Low execution time
  Bad at grasps
Harris Method
  Very good detection
  High execution time
  Good at grasps
Harris is the preferred method
  Future: Optimize (reduce points being tested)
    Reduce execution time
    Perfect detection
  Alternative:
    Feed Haar position into Harris
      Localize square in that location, return orientation
    Combine best aspects of both methods